NEW 12 KW Solar Generator, Off Grid on Trailer - $20000 (Riverside, CA)

condition: new
make / manufacturer: DC Solar
Brand new 12 KW, 120/240 volt solar generator mounted on a 10k lb GVW Carson trailer. Professionally built by DC Solar Company. Has ten, 235 watt solar panels which can be adjusted for best sunlight collection, Two SMA Sunny Island inverters, Midnight charge controller, Two 510 Ah 48 volt battery packs and assorted breakers and panels for controls and an integrated 11 KW 3 cylinder Diesel Kubota Generator (GL11000) with a 113 gal aux fuel tank. Two heavy duty 25 foot telescoping light towers with four each 120 watt LED high intensity area lights per tower. Lights have automatic on/off timers. Unit is fully automated for unattended operation. Perfect for lighting large areas, parking lots, security, off grid growers, etc. with the added benefit of having a 12kw aux diesel generator for any off grid use such as powering a home, work site or any other remote power requirements. The components on the unit individually cost about double my asking price. If you see this ad they are still available. I have 8 units total. Lastly, these may qualify for a 30% federal solar tax credit depending on how you utilize them. Check with your tax advisor to confirm.

Has two, 120/240 50-Amp Hubbell Twist 2 receptacles and four, 120V 20-Amp Receptacles

Has two, SMA Sunny Island Inverters (120/240 Volt AC Split Phase)
Continuous 12kW @ 120v200A

Has two, large 48 Volt Deep Cycle Industrial 510 Ah battery packs that weigh 2,000 lbs ea
1020 Amps Hours total @ 48V Nominal

Two 25 foot high telescoping light towers, one on each end of trailer, with four high power LED lights on each.

Total Solar Input is 2,350 Watts, with auto charging of batteries and automatic battery maintaining. Can run lights indefinitely on solar power only. Generator will automatically start/stop to charge batteries if needed.

Kubota model GL11000, 11 kw, 3 cyl Diesel generator with auto start and 113 Gallon fuel tank.
Fuel Consumption.75 gal/hr, Decibel Rating 68 db (A) @ 23 ft.

Trailer Dimensions
8'2" wide by 21'6" long by 8’ 4" high, Weight 8,500 lbs. With electric brakes and breakaway box. With Solar panels deployed, 11'11" max wide, height 5’ 4” min to 8'4" max depending on panel alignments.